## Slide 1: Unit 4 Memory and Basic Processor Interfaces
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Describe the basic components of random access memory
  Address and data bus, address decoder, storage
Identify which types of memory should be used for storage
  External vs. internal
  Registers vs. block memory
Describe and analyze timing for the AXI4-Lite protocol for reading and writing registers
Implement a simple IP with AXI4-Lite control registers using Vitis HLS
Synthesize and simulate the IP and analyze the timing diagrams
Deploy the IP on an FPGA board and interface with the IP via PYNQ

## Slide 3: Outline
Random Access Memory and Memory-Mapped Registers
Processor Interfaces with AXI4-Lite
Implementing AXI4-Lite Interface in Vitis HLS

## Slide 4: Addressable Memory
An array of elements in storage
  Use for vectors, matrices, packets, data, …
Word: Each of the data element
  Typically, has word / data width = 32 or 64 bits
Memory depth = number of words
Memory size=depth word width
Address: A location of a word
  Often byte-addressable
  Word is at byte address when word width=32
Byte address
Data
0
4
8
Word 0
Word 1
Word 2
Word
Example 32-bit memory with depth

## Slide 5: Sequential vs Random Access
Sequential Access
  Access time depends on position
  You must move through data in order
  Ex: Hard disks (seek + rotation)
  FIFO queues (logical sequential access)
Random access
  Any element can be accessed in constant time
  SRAM (on chip block memory, FPGA BRAM)
  DRAM (external memory)
  Register files (architecturally random access)

## Slide 6: Typical RAM Architecture
Three interface signals:
  Address input: Which word to select
  Read/Write: Which direction of transfer
  Data: Value to read or write
Address input:
  bits to select one of words
  Each word has a wordline select
  Selection determined by address decoder
Address input bits
Address decoder Selects one of
wordlines
wordlines
Data Bus
data words
R/W

## Slide 7: Bus
Bus: A shared communication pathway for multiple units
  Physically a set of wires
  For data, addresses, and control
  A shared protocol so only unit drives the bus at a time
Many examples:
  Multiple memory units connected to a common data bus
  A processor and multiple memory units sharing address or data
  Multiple peripherals on an SoC sharing an AXI bus
  Multiple devices on an or SPI bus
  …
Bus

## Slide 8: High Impedance
Method to share a common bus
  One unit drives a value on the bus
  Other units go into a high-impedance state, noted
  High impedance units are disconnected
  Bus value=
Sometimes called Tri-State
  Each bit is 0, 1 or Z
A
B
C
Bus
A | B | C | Bus Value | Remarks
Z | 15 | Z | 15 | B drives bus
41 | Z | Z | 41 | A drives bus
Z | Z | Z | X | No driver- no reliable value
32 | 78 | Z | X | Collision of A, B – no reliable value Protocols will avoid this condition

## Slide 9: High Impedance on a Data Bus
Memory read (Tri-State Bus)
  Selected memory element drives its value
  Other units go to
  Data bus value = selected memory element’s value
Memory write (Broadcast + Selective Capture)
  Data bus value appears at all units
  Selected element loads value into its storage element
  Other elements ignore value
Data Bus
data words
R/W

## Slide 10: External vs. Internal Memory
External memory
Off-chip
High capacity (GBs)
But need I/O to process
Internal memory
On-chip
Low capacity (KB-MB)
Direct access to processing
Low latency
Processing Hardware

## Slide 11: External vs. Internal Compared
SRAM cell
DRAM cell

## Slide 12: Example Memory Internal Sizes
Platform | On-Chip Memory Type | Typical Size | Notes
Laptop CPU (Intel Core) | SRAM (L1/L2/L3) | 20–40 MB | L3 dominates; very fast
NVIDIA A100 GPU | SRAM (L2 cache) | ~40 MB | HBM2e (40–80 GB) is off-chip/on-package
Xilinx Virtex-7 FPGA | BRAM (36 Kb blocks) | 2–6 MB | Distributed across fabric
Custom ASIC (5 mm² @16nm) | SRAM | 5–10 MB | Depends on layout & redundancy
Lesson: Internal memory is limited! Use judiciously.

## Slide 13: Example: Video
A video processor needs to store 8 frames of raw video
  512 512 pixels, 3 color channels, 8-bits per pixel
What is the memory capacity needed?
  pixels channels frames B/pixel 6.2 MB
  A sizeable portion of memory even on a large chip
If the data is stored as 32-bit words, how many words are in the storage
  There are 4B/word Mwords
How many address bits are needed assuming byte addressing?
  For byte addressing we need
  Smallest integer bits

## Slide 14: Registers vs. Block Memory
We have seen two storage types
Registers
  Typically implemented as flip-flops
  Useful for small, individual data pieces
  Control registers, intermediate calculations, …
Block memory
  Typically, DRAM or SRAM
  Ideal for large arrays
  Vectors or arrays
Block memory
Registers

## Slide 15: Memory Mapped Registers
Registers can also be memory-mapped
  Connected to their own address decoder
  Determines which register to read/write
Common interface to processor
  Processor sees registers & block memory together
  One continuous address space
Register address
decoder
Block mem
address decoder
ADDR bus
Data bus
Block memory
Registers

## Slide 16: Example
A HW module computes a cubic function:
Registers:
  Store polynomial coefficients
  Small, individual pieces
  Want parallel access
  Could have control registers, e.g. count, data valid, ready, …
Block memory
  Store input and output data
  and
  Ideal for large vectors
Block memory
Registers

## Slide 17: Outline
Random Access Memory and Memory-Mapped Registers
Processor Interfaces with AXI-Lite
Implementing AXI-Lite Interface in Vitis

## Slide 18: AXI4-Lite Protocol
ARM Extensible Interface family of protocols
  Others we will use in class are AXI4-Full and AXI4-Stream
Industry-standard, ubiquitously used
AXI4-Lite:
  Simple
  Ideal for programming registers
  Modular enables flexibility in delays and scheduling at both ends
  Typical throughput: 1 read / 1 write every 3-5 clock cycles

## Slide 19: AXI4-Lite Use Case: Processor to Hardware IP
Processor
E.g. ARM core
Hardware IP
Ex: FPGA module you have designed
Control registers
Bus signals
Address, data
Control
Widely-used use case
Hardware IP has control registers
Need read / write access from an embedded processor

## Slide 20: Master-Slave and Transactions
Processor
E.g. ARM core
Hardware IP
Ex: FPGA module you have designed
Control registers
Bus signals
Address, data
Control
In AXI4-Lite:
Each read or write of a single word is a transaction
Master: The unit that initiates all transaction (typically the processor in this example)
Slave: The unit that responds to the transaction (typically the hardware IP)
MASTER
SLAVE

## Slide 21: AXI4-Lite Write Protocol
Suppose master wants to write data to address
  AWADDR= and AWVALID=1
  WDATA= and WVALID=1
  Both can occur in independent clock cycles
When slave is ready for address or data it sets:
  AWREADY=1 and WREADY=1
  Slave can set these independently and any time it is ready
Transfer:
  When AWREADY=AWVALID=1 together address is transferred
  When WREADY=WVALID=1 together data is transferred
Handshake:
  After both are transferred, slave set BREADY=1
  Master sets BVALID=1 to acknowledge
  Can start next transaction in same clock cycle as BVALID=1
AWREADY
AWADDR, AWVALID
BVALID
WDATA, WVALID
WREADY
BREADY
MASTER
SLAVE

## Slide 22: Example AXI4-Lite Write
Transaction 4 cycles
Example with
Slave is ready before master
Address write before data write
But either order or together is fine

## Slide 23: Example AXI4-Lite Write With Stall
Transaction 4 cycles
Example:
Master sets valid
Slave is not ready
Transfer stalls
Provides flow control
  Ensures data waits until RX is ready

## Slide 24: Theoretical Optimal Write Throughput
Cycle 0:
  Master sets AWVALID=1, AWADDR= and WDATA= and WVALID=1
  Slave is ready: AWREADY=WREADY=1
  Both address and data are transferred to slave
Cycle 1:
  Slave set BVALID=1 signaling transaction complete on slave side
  Slave registers
Cycle 2:
  Master acknowledges with BREADY=1
  Master starts next transaction in same clock cycle
Theoretical optimal throughput = 1 word write / 2 clock cycles
Theoretical minimum latency = 2 clock cycles (master write + slave register)

## Slide 25: Practical AXI4-Lite Latency
Suppose:
  Master sets data and address on cycle 0
  Slave is ready
In most practical register systems:
  Slave takes 1-2 additional clock cycles for BREADY=1
Master takes at 1-2 additional clock cycles for BVALID=1 and next input
Practical throughput with AXI4-Lite: 1 word write per 3-5 clock cycles

## Slide 26: AXI4-Lite Read Protocol
Suppose master wants to read data from address
  ARADDR= and ARVALID=1
  Indicates that it wants to read data
When slave accepts the request:
  Sets ARREADY=1
When slave has fetched data:
  Sets RVALID=1, RDATA=
  Can be 0 to many cycles after ARREADY=1
Handshake:
  Master asserts RREADY=1 when ready to accept data
  RREADY could be asserted before RVALID=1
  Transfer completes when RVALID=RREADY=1
ARREADY
ARADDR, ARVALID
BVALID
RREADY
MASTER
SLAVE
RVALID, RDATA

## Slide 27: Example Read Timing
In this example:
Slave is initially ready (ARREADY=1)
Slave immediately accepts request
Master is immediately available for
Data valid with two cycle delay

## Slide 28: Theoretical Optimal Read Throughput
Cycle 0:
  Master sets ARADDR= and ARVALID=1
  Slave is ready: ARREADY=1
  Address is transferred to slave
Cycle 1:
  Slave set RVALID=1 with data RDATA=
  Master is immediately ready, RREADY=1
Cycle 2:
  Master moves to next read address
Theoretical optimal throughput = 1 word read / 2 clock cycles
Practical throughput = 1 word read per 3-5 clock cycles

## Slide 29: Outline
Random Access Memory and Memory-Mapped Registers
Processor Interfaces with AXI-Lite
Implementing AXI-Lite Interface in Vitis HLS

## Slide 30: Example: Connecting a Simple IP
ReLU + Linear
  Identical to Unit 1
Add an interface to a processor
  Processor can be an embedded
  Ex: ARM Core on Pynq board
  Interfaces to the IP over AXI4-Lite
Add control from host PC
  Ideally jupyter notebook
Linear + ReLU
Hardware “IP”
Memory- mapped registers
Processor system (e.g., ARM)
AXI4-Lite
Host PC
FPGA board

## Slide 31: HLS vs. RTL
RTL: Register Transfer Language
  Use specialized languages (e.g., SystemVerilog)
  Manually schedule action in each clock cycle
  Interfaces designed from scratch
  High control, supports custom interfaces
  But time-consuming, difficult to maintain
HLS: High-Level Synthesis
  Write in general purpose languages (e.g., C++)
  Clock-level schedule determined automatically by compiler
  API support for common interfaces (e.g., AXI)
  Sacrifice some performance and flexibility
  But enables rapid development

## Slide 32: HLS vs. RTL FPGA Design Flow
Traditional RTL Design Flow
  Designer directly writes RTL
  Tools simulate and synthesize
HLS Flow
  Designer write high-level language (e.g., C)
  Standard software compile-synthesis
  RTL files auto-generated
RTL Simulate
Package
RTL Simulation
Package
Human-written RTL files (e.g. SV)
C Synthesis
C simulation
Auto-generated RTL files
Human-written C files

## Slide 33: Bad vs. Good HLS Code Write
Bad: Treat HLS tool as a black box
Results in RTL code with poor performance
No way to evaluate if resulting design is good
Good: Have a mental model
Think what the RTL code should look like
What should happen on each clock cycle
What resources should be used
RTL Tool
HLS Tool
RTL Tool
HLS Tool
Mental RTL model

## Slide 34: Vitis HLS
Developed by Xilinx (now AMD)
  Evolved from Vivado HLS
Supports C / C++
  Simple, common development
Some python support for testbenches
Ships with Vitis IDE
Native support for AXI protocols
  No need to build handshake from scratch

## Slide 35: FPGA Board Components
We target a design on a real FPGA board
Boards have three components
Processing system (PS)
  A lightweight processor
  Often an ARM core
  E.g., ARM A9
Programmable logic (PL)
  The programmable fabric
  This is where your IP will reside
  Also contains the registers and internal memory
An AXI4 interface
Image from MathWorks page on embedded design

## Slide 36: Target Architecture
Linear + ReLU
Hardware “IP”
Memory- mapped registers
PS
AXI4-Lite
Host PC
Pynq Z2 board
PL
We will rapidly build
Complete AXI4-Lite I/F
  Interface done automatically
  No need to code any handshaking
Control through host
  Simple python jupyter notebook
Deploy to a real FPGA!

## Slide 37: IP Source Code
IP Source Code is simple
Module declaration
Port descriptions
Main functional description

## Slide 38: Module Declaration
Module declaration
  Defines inputs and outputs
  Standard C

## Slide 39: Module Declaration
Port definitions
  Use pragma statements
  Do not change function
  But tell synthesizer how to map to hardware
  Indicates ports are axislite (AXI4-Lite slave)
  Share a common bundle (all on the same AXI4-Lite interface)
  Additional port=return (Provides start, stop, see later)

## Slide 40: Module Declaration
Main function definition
  Plain C
  Do not specify the implementation Just the desired behavior
  Synthesizer may map to multiple clock cycles
  You do not have to do scheduling manually

## Slide 41: Vitis HLS Testbench
Testbench
  Program simulating another unit interacting with IP
  IP is the device-under-test (DUT)
In HLS:
  Testbench another C program
  Calls the DUT module like a C function
  Sequential behavior
  Testbench code can use any C / C++ functions
  Does not need to be “synthesizable”

## Slide 42: Vitis HLS Flow Described in Flow Panel
Tool follows expected steps for HLS flow
RTL Simulation
Package
C Synthesis
C simulation
Auto-generated RTL files

## Slide 43: Synthesis Output
Resulting Verilog files are massive!
Main function in this case:
  simp_fun.v
  > 200 lines of Verilog
  Hard to read code
You saved a lot of time coding

## Slide 44: Synthesis Report
Generate a Report in Vitis Tool
  Later, we will write python to parse these
Timing estimate
  Timing of critical path
  Can verify that lower than clock period
Estimated latency
  In this case = 4 clock cylces
Estimate resources
  Amount of each FPGA resources used
  BRAM, DSP, …
  We will discuss these in detail later

## Slide 45: RTL Simulation
Run RTL sim and extract VCD diagram
Left plot:
  One transaction with IP
  Can visualize AXI4-Lite interaction
Write:
  Write three values:
  3 clock cycles each
Read:
  Reads output
  Approximately 20 cycles after first write

## Slide 46: RTL Simulation over Multiple Interactions
Approximately 20 cycles for each input
We will be able to do this much faster
  Will use an AXI-Streaming interface
  Next lecture
AXI4-Lite is design for slowly varying items

## Slide 47: Execution Model
Write phase
  PS writes input control registers
  PS “start” on the control register
  Transaction starts when “ready”
  IP asserts “done”
  PS reads outputs

## Slide 48: Deploying on an FPGA Board
Will show this in class