## Slide 1: Unit 5 FIFOs and Streaming Interfaces
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Describe the operation and work out the timing of FIFO reads and writes
Describe and simulate the AXI4-Streaming protocol
  Pure streaming interfaces
  Packetized streaming interfaces
Design simple streaming modules in Vitis HLS
Design robust command and response packets with:
  Transactions IDs for detecting missed packets and error codes
Write serialization and deserialization methods
  Manually and using an interface description language
Implement packet-based streaming modules in Vitis HLS

## Slide 3: Outline
FIFO Interfaces
AXI4 Pure Streaming Interface
Limitations of Pure Streaming with Vitis
AXI4 Packetized Streaming

## Slide 4: FIFO Motivation
To motivate FIFOs, we review two problems we have encounter
Problem 1: Low throughput on transfers with handshakes
Problem 2: Idle time on systems with polling

## Slide 5: Problem 1: Handshaking Overhead
Transaction 4 cycles
Last Unit: Transfers with handshake
  Slave asserts READY
  Master assert VALID
AXI4-Lite
  Each read or write takes 2 to 4 cycles
Provides:
  Guaranteed delivery
  Flow control
But adds overhead

## Slide 6: Problem 2: Polling-Based Execution
Execution model in previous unit:
  PS writes input data
  PS sets ap_start
  IP processes data
  PS poll ap_ready until complete
  PS reads output
Processing System (PS)
VITIS HLS IP
ap_start
ap_ready
Write input
Read output

## Slide 7: Problem 2: Time Wastage
Several overhead times on both the PS and IP
  Transfer: PS spends time transferring data in and out of IP
  Polling: PS must poll while IP is processing
  Idle: IP is idle during transfer and wait for control

## Slide 8: FIFO
Producer
Consumer
FIFO (First-In First-Out) hardware queue
  Stores data from a producer in order of arrival
  Returns data to a consumer in same order
Decouples producer and consumer timing
  Each side can run at their own pace
Built-in flow control
  Producer checks if FIFO is full
  Consumer checks if FIFO is not empty
Absorbs bursts of data
Enables streaming behavior

## Slide 9: FIFO Terminology
Producer: Module that writes to FIFO
  Each write adds an element
Consumer: Modules that reads from FIFO
  Each read removes an element
Element: Logical item stored in the FIFO
Element width: Size of each element
  Typically, in bytes or bits
Depth: Maximum number of elements
Producer
Consumer
FIFO element
Element width
Depth

## Slide 10: FIFO Order
Suppose FIFO writes A, B, C
Then:
  A is at the head of the queue
  C is at the tail
Consumer reads from the head
Will read in order A, B, C
Same order as the write
A
B
C
Producer writes A, B, C, …
Consumer reads A, B, C
Tail
Head

## Slide 11: Example Problem

## Slide 12: Example Problem

## Slide 13: Solution

## Slide 14: FIFO Overflow
Suppose producer tries to write an element when FIFO is full
Two possible behaviors
Blocking write
  FIFO signal not READY
  Producer waits
  Default behavior in most hardware interfaces (including AXI-Stream)
  Also called stall, backpressure or flow control
Drop
  Drops some packet in queues
  Head, tail, or random
  Common in network routers
Producer
Consumer

## Slide 15: Example Problem

## Slide 16: Solution

## Slide 17: Producer and Consumer Rate
Producer rate = average number of elements to write per unit time
  Time unit can be clock cycle, seconds, etc
  If producer is sending jobs, producer rate = workload rate requirement
Consumer rate = maximum number of reads per unit time
  If consumer processes element, consumer rate = maximum work throughput
Load factor:

## Slide 18: Load Factor and Stability
Condition | Queueing theory term | Hardware term | Implication
 | Stable | Under-utilized; headroom available | FIFO will always eventually drain. No necessary drops / stalls. But short-terms drops / stalls may be possible
 | Critical | Fully utilized | Stalls / drops may or may not occur.
 | Unstable | Overloaded, over-subscribed | With backpressure, producer will have infinite backlog. Without backpressure, some elements will be dropped
Condition | Queueing theory term | Hardware term | Implication
 | Stable | Under-utilized; headroom available | FIFO will always eventually drain. No necessary drops / stalls. But short-terms drops / stalls may be possible
 | Critical | Fully utilized | Stalls / drops may or may not occur.
 | Unstable | Overloaded, over-subscribed | With backpressure, producer will have infinite backlog. Without backpressure, some elements will be dropped

## Slide 19: Sample Problem

## Slide 20: Solution

## Slide 21: Queueing Theory
Models arrivals and departures probabilistically
Used widely in networking research
  Determine probabilities of buffer overflow
  Optimal routing and drop policies
  Also used in network on chip
But requires mathematics
  Markov chains, probability
Take NYU’s networking theory class if interested

## Slide 22: Outline
FIFO Interfaces
AXI4 Pure Streaming Interface
Limitations of Pure Streaming with Vitis
AXI4 Packetized Streaming

## Slide 23: Problem 1: Handshaking Overhead
Transaction 4 cycles
Last Unit: Transfers with handshake
  Slave asserts READY
  Master assert VALID
AXI4-Lite
  Each read or write takes 2 to 4 cycles
Provides:
  Guaranteed delivery
  Flow control
But adds overhead

## Slide 24: Solution: Streaming FIFO Interface
Consider a PS sending jobs to accelerator
Use FIFOs for jobs and responses
Decouples for timing
  Transfer of data of the PS
  Processing of data in the HW
Enables efficient burst transfers
  Many elements can be transferred at once
  Reduces handshaking overhead
Both PS and HW run at their own pace
If some jobs need a lot of time
  Job FIFO buffers the jobs to process
Processing System
Job FIFO
Response FIFO
Processing Engine
Hardware accelerator

## Slide 25: AXI4-Streaming Protocol
Industry standard streaming protocol
  Available as the interface to many Xilinx IP blocks
Pre-built in Vitis HLS
  All FIFO management is done for you
Part of the AXI4 family:
  AXI4-Lite: Covered last unit
  AXI4-Stream: This unit
  AXI4-Memory mapped: Later
Provides a simple interface with DATA, READY, VALID
Additional capabilities (covered later in this unit):
  Packetization
  Addressing
Processing System
Response AXI4-stream
Processing Engine
Hardware accelerator
Command AXI4-stream

## Slide 26: AXI4-Stream Terminology
Each AXI4-Stream is uni-directional
Master is the producer / sender
  Could be PS sending jobs or HW accelerator returning responses
Slave is the consumer / receiver
  Could be PS receiving response or HW accelerator receiving jobs
FIFO is typically realized on the
MASTER
SLAVE
FIFO
AXI4-Stream

## Slide 27: AXI4-Stream Protocol
Slave asserts TREADY on any cycle it can accept data
  Typically, when FIFO has space
On any cycle has data to transfer, master:
  Places data on TDATA
  Asserts TVALID
If TREADY=TVALID=1, there is a transfer
  Otherwise, master can re-assert TVALID on next cycle
Slave processes FIFO at its own pace
  Backpressure to master via TREADY
Can transfer up to data element
MASTER
SLAVE
FIFO
TDATA
TVALID
TREADY

## Slide 28: Example Timing
Cycle | Master action | TVALID | TREADY | FIFO | Slave action | TREADY for next cycle
0 | Transfer A | 1 | 1 | [A] | - | 1
1 | Transfer B | 1 | 1 | [B] | Read A | 1
2 | Transfer C | 1 | 1 | [C,B] | Process A | 0
3 | D stalls | 1 | 0 | [C] | Read B | 1
4 | Transfer D | 1 | 1 | [D,C] | Process B | 0
5 | E stalls | 1 | 0 | [D] | Read C | 1
6 | Transfer E | 1 | 1 | [E,D] | Process C | 0
Master always has data
  TVALID=1 always
Slave takes 2 cycles to:
  Read data
  Process data
FIFO depth = 2

## Slide 29: Example: Streaming Squared Average
Given:
  Input stream
Compute output stream:
  is a fixed window size
Models an average power
Use AXI4-Stream for and
Polynomial Eval
Hardware accelerator
Input stream
Input stream
AXI4-Stream

## Slide 30: Vitis HLS Module Definition
Input and output streams
Declares that variables are AXI4-Stream Does not state if master or slave.
Declares that module has no explicit start stop

## Slide 31: Vitis HLS Module Body
Reads input data
Computes average of current + past 2 values.
Outputs past values
Writes output

## Slide 32: In-Class Demo
We will perform
C simulation
C synthesis
RTL co-simulation
VCD extraction

## Slide 33: Simulation Results

## Slide 34: Outline
FIFO Interfaces
AXI4 Pure Streaming Interface
Limitations of Pure Streaming with Vitis
AXI4 Packetized Streaming

## Slide 35: Limitations of Pure Streaming
Problem 1: Many operations fundamentally operate in blocks
  Pure streaming interface does not natively have a block boundary
Problem 2: Hard to synchronize control and data
Problem 3: Vitis is not well-equipped to simulate continuous kernels
  Vitis has a fundamentally flawed execution model

## Slide 36: Problem 1: Block-Based Operations
Many problems naturally work on blocks
Need to know boundaries
Ex: Image processing
  Each input is a image
  Images have a first and last element
  Scanned in some particular order (e.g. row-wise)
Ex 2: Matrix multiply
  Module needs two matrices
  Each has to be read in some order
Pure streaming is not natively good for these operations
Individual elements
Blocks of elements

## Slide 37: Problem 2: Control-Data Synchronization
This problem is more subtle
Consider a parametrized streaming function:
  : some parameter that changes slowly
For example, streaming polynomial:
Polynomial Eval
Hardware accelerator
Input stream
Input stream
Control

## Slide 38: Solution: Mix AXI4-Lite and AXI4-Stream?
Given:
  Input stream
  Polynomial coefficients (change slowly)
Compute output stream:
Set coefficients via AXI4-Lite
  Assume they change slowly
  Do not need fast read / write
  But benefit from continuous access
Use AXI4-Stream for and
Polynomial Eval
Hardware accelerator
Input stream
Input stream
AXI4-Lite
Coefficients
AXI4-Stream

## Slide 39: A Potential HLS Module Definition
Coefficients
Input and output streams
Declares that variables are AXI4-Stream Does not state if master or slave.
Direction will be inferred
AXI4-Stream FIFO depth
Declares that coefficients are AXI4-Lite

## Slide 40: Problem Mixing AXI4-Lite and AXI4-Stream
Problem: How do we synchronize control and data?
Control and data are typically fed by different sources
Exact timing of control is indeterminate.
Bad: “Change control around now”
Good:
  Index samples by
  “Apply this control precisely on sample ”
This synchronization needs additional logic
Polynomial Eval
Hardware accelerator
Input stream
Input stream
AXI4-Lite
Coefficients
AXI4-Stream

## Slide 41: Problem 3: Vitis’ Flawed Execution Model
Software
developer
I need to
accelerate this step
Vitis generated RTL equivalent code
  Drop-in replacement for SW call
  Called with sequential manner

## Slide 42: Vitis Execution Model Flaws
Item | Vitis Assumption | Proper hardware model
Execution paradigm | Module is “called” like a C function | Modules operate continuously and respond to events
Interface | C-like call | Hardware channels e.g., FIFOs and memory-mapped interfaces
Concurrent behavior | Obscured | Made explicit
Hardware is not software

## Slide 43: Outline
FIFO Interfaces
AXI4 Pure Streaming Interface
Limitations of Pure Streaming with Vitis
AXI4 Packetized Streaming

## Slide 44: Pure vs. Packetized Streaming
Pure streaming
  Module processes one data element at a time
  Ex:
  Control (e.g., ) set in a separate path
Packet streaming
  Module processes data in blocks or packets
  Control may be sent with packet
HW module
Control
Input data
Output data
HW module
Control
Data
Control
Data

## Slide 45: AXI4-Stream Protocol with Packetization
Add a TLAST line
TLAST = 1 on the last transfer
Indicates the end of packet
Packets are transferred in bursts
  Begins with first TVALID = 1
  Ends TLAST=1 and successful transfer
Cycles in a burst are called beats
  Transfer beat (TVALID=TREADY=1)
  Idle beat (TVALID=0)
  Stall beat (TVALID=1, TREADY=0)
  Last beat (TVALID=TREADY=TLAST=1)
MASTER
SLAVE
FIFO
TDATA
TVALID
TREADY
TLAST

## Slide 46: Example Burst Timing
TDATA | TVALID | TREADY | TLAST | Beat Type
A | 1 | 1 | 0 | A transfers
B | 1 | 0 | 0 | B stalls (Slave not ready)
B | 1 | 1 | 0 | B transfers
- | 0 | 1 | 0 | Idle (Master has no data)
C | 1 | 1 | 0 | C transfers
D | 1 | 0 | 1 | D stalls
D | 1 | 1 | 1 | D transfers with end of burst

## Slide 47: Example Burst Timing Illustrated
7 Beats and 4 Transfers

## Slide 48: Example: Block Polynomial Accelerator
Given:
  Input stream
  Polynomial coefficients (change slowly)
Compute output stream:
Idea: In each burst transfer
  Coefficients
  Length
  Data
Polynomial Eval
Input stream
Output stream
AXI4-Stream

## Slide 49: Command Packet Structure
Transaction ID (see later)
Coefficients
Length
Command Header
Data

## Slide 50: Response Packet Structure
Transaction ID
Response Header
Data
Response Footer
Error code Num read

## Slide 51: Serialization / Deserialization
Packets have arbitrary:
  Structure (often different fields)
  Arbitrary, sometimes variable, length
Hardware streams have specific bit widths
  Ex: 32, 64, 128, …
  Each stream element is a word
Serialization: Converts packets to array of stream words
Deserialization: Streams words to packets
uint32 words
Packet
uint32 words

## Slide 52: Serialization / Deserialization Illustrated
TX Packet
Serialization
Stream words (e.g., ap_uint<32>)
Stream words
RX Packet
AXI4-Stream
Deserialization

## Slide 53: Serialization / Deserialization in Hardware
Python and C++ have widely-used serialization tools
Ex: Python pickle
  Can serialize an arbitrary class
  Serializes complex nested structures
Ex: Boost.serialization
  Similar package in C++
No standard library in hardware
Often write custom serialization

## Slide 54: Example Problem

## Slide 55: Solution: Counting the Number of Words

## Slide 56: Solution: Serialization Code

## Slide 57: Vitis HLS Module Definition
Input and output streams
Declares that variables are AXI4-Stream Does not state if master or slave.
Declares that module has no explicit start stop

## Slide 58: Vitis HLS Command and Response Header
Deserialize command header
Write response header Each transaction ID

## Slide 59: Main Process Loop
Read word
Compute polynomial
Write to output stream

## Slide 60: Response Footer and Error Handling
Check for synchronization error
  TLAST not in expected position
If there are errors:
  Sends response with error code
  Flush queue to next TLAST
Key design error handling principles:
Hardware cannot terminate.
It must self-recover
Must provide visibility to errors

## Slide 61: In-Class Demo
We will perform
C simulation
C synthesis
RTL co-simulation
VCD extraction

## Slide 62: Simulation Result

## Slide 63: Using an Interface Description Language
Most professional designers do not hand write their serialization
  Error prone, tedious
The class xilinxutils package has a simple interface description language:
  Serves as a master description for python and Vitis

## Slide 64: Vitis HLS Code Generation
The python descriptors can be used to autogenerate the Vitis HLS header files
No need to manually write the serialization
Auto-generated