## Slide 1: Unit 6 Timing and Critical Path Analysis
EL-GY 9463: Introduction to Hardware Design
ProfS. Sundeep Rangan, Siddharth Garg

## Slide 2: Learning Objectives
Define undefined and stable periods for logical signals
Compute the maximum propagation delay of combination logics
  Series circuits, conditional, multi-path
Perform static timing analysis of sequential logic
  Determine the critical path of a circuit
  Determine maximum frequency and detect timing violations
Draw timing diagrams, both real and cycle-accurate
Describe timing via value-change points
Extract VCD files from Vitis and display timing information in python

## Slide 3: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams from Vitis

## Slide 4: Static Timing Analysis
Timing analysis: Estimate delays through circuits
Visualize with a timing diagram
Critical for estimating:
  Clock speed, latency, throughput, …
Static timing analysis:
  Focus on maximum propagation delay
  Timing that can be guaranteed for all inputs
  Not data dependent
This analysis is conservative, but provides hard guarantees
Default analysis in industry

## Slide 5: Implementing Signal Physically
To understand timing, we need to look at physical implementation of signals
Consider a binary signal from Unit 1
Two logical values: 0 or 1
What happens physically?
  Typically, a voltage on a wire
  Takes a continuous value
  Obtain logical value by thresholding

## Slide 6: Undefined Logic Value: ‘X’ or ‘?’
Signals take time to transition
  They are outputs of physical circuits
  Gates, computational units, …
Creates an undefined period
  Also called indeterminate, unknown, …
Usually denoted as X
  We may use ? to avoid confusion with variable
So binary logic signals have three values:
  0, 1 and X
  Will discuss a fourth value Z later
0
X
1
X
0

## Slide 7: Undefined Regions Illustrated
Analog physical signal
  Typically, a voltage
  Continuous valued
  Has finite transition periods
Digital logic signal
  Three values 0, 1 and X
  X value shown in gray
X
X
X
X
X

## Slide 8: Stable Values and Propagation Delays
Stable value: Eventual value after a transition
  Ex: Suppose and transitions from 4 to 5:
  Output is eventually
  Stable output value is
Propagation delay:
  Time for the output to transition
Two components:
  Logic delay: Time for the logic gates to settle
  Routing delay: Time to pass through wire
  May be related to capacitance, current source limits
ns
ns

## Slide 9: Maximum Propagation Delay
Actual delays vary
  Signal length, temperature, device variability
Typically use maximum propagation delay
Timing diagrams show max propagation delay
X region represents:
  Region where value cannot be guaranteed
  Often stable before max delay
Max propagation delay often very conservative
  Real propagation delay may be maximum
  Violating delay is usually catastrophic
Worst-case ns
X

## Slide 10: Timing in a Series Circuit: ReLU + Linear
As example, consider a more complication circuit:
  Linear function + ReLU from Unit 2
  Used widely in machine learning
Output port
Input ports

## Slide 11: Timing Diagram for Series Connections
Linear + ReLU can be implemented as a series connection
  In this case, three operations one after the other
For analysis, assume the max propagation delays in the table
Question: What does the timing diagram look like with changes in the input?
Hardware block | Max prop delay
Multiplier | 3 ns
Adder | 1.5 ns
Max operator | 1 ns
Total | 5.5 ns
Hardware block | Max prop delay
Multiplier | 
Adder | 
Max operator | 
Total | 

## Slide 12: Timing Diagram of a Series
Suppose are invalid for
  They are in a transition in this period
  Signals are unknown X
Mark the unknown region with violet [0,2]
When are downstream signals stable?
?
[0,2]

## Slide 13: Series Timing: Initial Component
Start with first component (multiplier)
Inputs are invalid in [0,2]
Max propagation delay of mult = 3 ns
Mult_out is invalid from [0,5]
  Invalid for 3 ns longer than input
Final stable value:
  Mult_out = 3*10 = 30
?
[0,2]
[0,5]

## Slide 14: Series Timing: Second Component
From previous slide:
  Mult_out is invalid from [0,5]
Adder max propagation delay = 1.5 ns
Hence add_out invalid in [0,6.5]
Observe: For worst-case analysis
  Add_out is invalid immediately when is invalid
Invalid propagates immediately
Stable conditions propagate with delay
?
[0,2]
[0,6.5]
[0,5]

## Slide 15: Series Timing: Third Component
Similar logic as add_out
Add_out is invalid [0,6.5]
Max logic has max prop delay = 1 ns
Output is invalid in [0, 7.5]
Total propagation delay = 5.5 ns
  Period after inputs were stable
[0,2]
[0,6.5]
[0,5]
[0,7.5]

## Slide 16: Example Total Propagation Delay
Hardware block | Example Value
Multiplier | 3 ns
Adder | 1.5 ns
Max operator | 1 ns
Total | 5.5 ns
Hardware block | Example Value
Multiplier | 
Adder | 
Max operator | 
Total | 
ns

## Slide 17: Example Timing Over Multiple Inputs

## Slide 18: Example Problem

## Slide 19: Typical Propagation Delays: Low-End FPGA
Hardware block | FPGA resource | Typical range
32-bit adder | LUT + dedicated carry chain | 1.5–3.0 ns
16-bit multiplier | DSP48E1 block | 2.5–5.0 ns
16-bit comparator | LUT logic + carry chain | 1.0–2.0 ns
Rough delays for a low-end FPGA (e.g., Pynq Z2)
We will explain the FPGA resources more in later units
Routing delays not included
  May be large for more complex designs

## Slide 20: Typical Propagation Delays: ASIC
Hardware block | Typical structure | Typical range
32-bit adder | Kogge‑Stone / Brent‑Kung / hybrid | 150-450 ps
16-bit multiplier | Wallace/Dadda tree + final adder | 300-700 ps
16-bit comparator | XOR/AND/OR chain with early‑out | 50-300 ps
Rough delays for TSMC 16nm
Custom ASICs are much faster than FPGAs
  Easily 5 to 10x faster

## Slide 21: Timing Diagram with Multiple Paths
Now consider a circuit with multiple paths
Input to the adder has two paths:
  One from xsq
  Second from ReLU function r
How does the timing diagram work?

## Slide 22: Timing Diagram: Inputs
s
Suppose input:
  Transitions from to 4
  Transition interval is (marked as X)
?
[10,12]

## Slide 23: Timing Diagram: First Steps
s
Square output
  Multiplication max delay is 3
  Value X from [10, 15]
  Then comes to stable value 16
ReLU output
  ReLU max delay is 1
  Value X from [10, 13]
  Then comes to stable value 4
These steps operate in parallel
?
[10,13]
[10,12]
[10,15]

## Slide 24: Multipath: Final Output
Output has two inputs
  and
Output goes invalid when either input = X
  Both are invalid starting at
  So, y is invalid starting at
Propagation delay starts when both are stable
  Before this output cannot be guaranteed
  is stable at
  is stable at
  Propagation for adder is 1.5
  stable at 16.5
[10,16.5]
[10,12]
[10,15]
[10,13]

## Slide 25: Conditional Circuits
Consider conditional block
How is it implemented?
What is the max propagation delay?

## Slide 26: Implementing Conditional with Multiplexers
Multiplexer:
  Circuit that selects one of a set of inputs
  Uses a condition input
Inputs and conditions
  All computed in parallel
  But each need distinct hardware
No savings in hardware dependent on data
  All possible inputs must be computed
Propagation delay starts with slowest input

## Slide 27: Propagation Delay with Multiplexers
Values in violet are max prop delay
Slowest of the mux input and condition:
  branch is the slowest
  Takes 4 ns
  Mux adds 1 ns
  So is stable at 5 ns
Output is stable 1.5ns after
4
2
0.5
5+1.5=6.5
4+1=5
4

## Slide 28: Critical Path
Critical path:
  The path with the largest max propagation delay
In this case:
To reduce overall max propagation delay:
  Must reduce max delay on critical path
For example:
  Reducing delay of will reduce critical path
  But reducing does not help
2
0.5
6.5
5
4

## Slide 29: Critical Path Example
Example: For some functions
Path 1 ():
  Delay = 3+2+2.5 = 7.5 ns
  Longest = Critical path
Path 2 (:
  Delay = 3.5 + 2.5 = 6 ns
  Shorter = Non-critical

## Slide 30: Delay Depends on Implementation
Example: Consider
Suppose each add takes seconds
Synthesis tools try to find low delay implementations
Serial implementation
Prop delay =
Parallel
Prop delay =

## Slide 31: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams from Vitis

## Slide 32: Synchronous Logic
We now perform static timing analysis for synchronous logic
This unit, we assume
  All registers clocked on a common positive clock edge
  All registers are perfectly synchronized (no clock skew)
  No asynchronous reset

## Slide 33: STA for Synchronous Logic Overview
STA considers all register-to-register paths
  Every register output to register input
Tests two conditions
No paths arrive too late
  Signals must arrive before next transition
  Must meet a set-up time and clock-to-Q time
No paths arrive too early
  Min delay > hold time
  Registers inputs must be stable for a hold period

## Slide 34: Set-Up and Hold Time
Registers typically implemented with a flip-flop
  Sometimes called D-Q flip-flop
Stable operation requires:
  Inputs are stable before and after clock edge
Set up margin:
  Time from stable to rising clock edge
  Requirement: Set-up margin > set-up time
Hold margin:
  Time stable after rising clock edge
  Requirement: Hold margin > hold time
Setup margin
Hold margin
(min)
set-up time
(min) hold time

## Slide 35: Clock-to-Q time
Clock-to-Q time
  Time from rising edge to stable output
Sometimes loosely called register delay
Physically time to transfer input to output
Clock-to-Q time

## Slide 36: Typical Times
Note: Modern nodes may have a negative hold time!

## Slide 37: Register-to-Register Paths
Register-to-register paths
  Start at any register output
  End at any register output
Can be visualized on a dataflow graph
  Maps logics and register for each update
  Primed values represent values in next cycle
In this example, there are four paths

## Slide 38: STA Analysis: Verifying the Set-Up Time
For now: Assume min hold time condition is met
  We will address this later
Must verify the set-up time condition:
  Max path delay
  All paths arrive within set up period before clock edge
Path delay has two components
  = Combinational propagation delay
  One clock-to-Q delay
Now = Max PD of critical path
  Measured in combinational circuit
Hence, to meet timing we need:
Combinational PD
Clock-to-Q time

## Slide 39: Meeting or Failing Timing
From previous slide, assuming minimum hold time condition is met:
  = clock period, clock frequency
  delay of critical path in combinational logic
  = min set up time, = Clock-to-Q time
If condition is satisfied, say system meets timing
Otherwise, system fails timing / timing violation
To meet timing:

## Slide 40: Example: Calculating Critical Path
Max propagation delay
  Can be computed recursively
  Identical to combinational section
Component | Value [ns]
PD | 1.8
PD | 2.2
PD | 2.1
PD | 2.3
 | 0.2
 | 0.1
Component | Value [ns]
 | 1.8
 | 2.2
 | 2.1
 | 2.3
 | 0.2
 | 0.1
1.8
2.2
2.2+2.3 =4.5
1.8+2.1 =3.9
3.9+0.2=4.1
4.5+0.2=4.7

## Slide 41: Example: Maximum Clock Frequency
From previous slide:
  Critical path delay in combination logic: ns
Therefore, to meet timing: ns
Max clock frequency
Component | Value [ns]
 | 4.5
 | 0.2
 | 0.1
min | 4.8
Component | Value [ns]
 | 4.5
 | 0.2
 | 0.1
 | 4.8
4.5
4.5+0.2=4.7

## Slide 42: Meeting the Min Hold Time Constraint
Consider circuit to the right
  A simple delay line
Naïve implementation
  Very short path: Output input
  Could violate minimum hold time
Typical solved in place & route
  Physical design will insert delay elements
With reasonable synchronous design:
  RTL design does not need to worry about this constraint
Short path. Could violate min hold

## Slide 43: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams from Vitis

## Slide 44: Synchronous Logic Detailed Timing Diagram
Consider counter:
Two delays in any synchronous circuit
Clk-to-Q delay: clock rising edge register output
  This example shown as 2 ns
Combinational PD: register output next value
  This example shown as 3 ns

## Slide 45: Detailed Timing Diagram
Timing diagram drawn called detailed diagram
  Sometimes called the real timing diagram
Shows all details:
  Register delays
  All propagation delays in combinational paths
Good for reasoning about precise timing
  Can compute computation speed, throughput, …
But too many details to understand functionality

## Slide 46: Abstract or Cycle Accurate Timing Diagram
Abstract timing diagram
  Also called cycle-accurate diagram
  All delays 0
  Ignores computation time
No unknown (X or ?) regions
Simpler to see functionality
Values in each cycle represent
  Value immediately before rising edge at end of cycle
Delays 0
Detailed timing diagram
Abstract timing diagram

## Slide 47: ReLU + Linear Synchronous Module
Now consider synchronous version of ReLU + linear
Identical to Unit 2
We add two inputs to ports
  Clock signal
  Reset on negative edge
Clock
Reset

## Slide 48: Synchronous Implementation
Use identical implementation as in Unit 2
Next values computed in always_comb block

## Slide 49: STA
Assume the propagation delays in table
Delay in each stage shown in violet
Ignore CLK-Q time
Hardware block | Max prop delay
Register | 0 ns
Multiplier | 3 ns
Adder | 1.5 ns
Max operator | 1 ns
Total =critical path | 5.5 ns
Hardware block | Max prop delay
Register | 0 ns
Multiplier | 
Adder | 
Max operator | 
Total =critical path | 
0
0
3
0
3+1.5=4.5
4.5+1=5.5

## Slide 50: ReLU+Linear Timing Diagram
Hardware block | Example Value
Multiplier | 3 ns
Adder | 1.5 ns
Max operator | 1 ns
Total =critical path | 5.5 ns
Hardware block | Example Value
Multiplier | 
Adder | 
Max operator | 
Total =critical path | 
ns
ns
Meets timing:

## Slide 51: Max Clock Frequency Example
ns
ns
Max clock frequency in our example:
  Min ns
  Max clock frequency = MHz

## Slide 52: Quadratic Example
Consider a quadratic function:
For simplicity, assume are fixed parameters
Single cycle implementation to the right

## Slide 53: Finding the Critical Path
Consider implementation with times in table
Two paths:
Path 1: x, x_reg, xsq_w2, y
  1 register, 2 mults, 2 adders = 12 ns
Path 2: x, x_reg, x_w1, y
  1 register, 1 mult, 2 adders = 8 ns
Path 1 is critical
Max clock frequency MHz
Would fail timing at MHz
Hardware block | Example Value
Register | = 1 ns
Multiplier | = 4 ns
Adder | 1.5 ns
Path 1 | 1+4+4+1.5+1.5 = 12
Path 2 | 1+4+1.5+1.5=8
Hardware block | Example Value
Register | 
Multiplier | 
Adder | 
Path 1 | 1+4+4+1.5+1.5 = 12
Path 2 | 1+4+1.5+1.5=8

## Slide 54: A Two Cycle Design
We can improve throughput by breaking computation over two cycles
Register two intermediate terms:
  xsq = xreg * xreg
  lin_term = w1*xreg + w0

## Slide 55: Three Stages
Design is processed in three stages = 2 cycles
Stage 0
  Register input to xreg
Stage 1: Compute and register:
  xsq = xreg * xreg
  lin_term = w1*xreg + w0
Stage 2: Compute output
  y = w2*xsq + lin_term

## Slide 56: Critical Path with Three Stages
Measure paths from register to register
Path 1: x, x_reg, xsq input
  1 register, 1 mult = 5 ns
Path 2: x, x_reg, w1_x, lin_x input
  1 register, 1 mult, 1 add = 6.5 ns
Path 3: xsq_reg, lin_x, w2_xsq, y
  1 register, 1 mult, 1 add = 6.5 ns
Critical path delay = 6.5 ns
Max freq = MHz
Hardware block | Example Value
Register | = 1 ns
Multiplier | = 4 ns
Adder | 1.5 ns
Path 1 | 1+4=5
Path 2 | 1+4+1.5=6.5
Path 3 | 1+4+1.5=6.5
Hardware block | Example Value
Register | 
Multiplier | 
Adder | 
Path 1 | 1+4=5
Path 2 | 1+4+1.5=6.5
Path 3 | 1+4+1.5=6.5

## Slide 57: Two Cycle Timing Diagram
Example with
inputs 10, -4, 8

## Slide 58: Latency, Throughput and Pipelining
Suppose that we run at our design at 100 MHz clock
Latency:
  Suppose input is valid on rising edge of clock
  Then output is valid before rising edge of clock
  Latency = 2 clock cycles = 20 ns
Throughput:
  Circuit can take a new input each cycle
  Throughput = 1 input / cycle = MHz
Process is called a pipeline
  Circuit is processing multiple inputs at the same time

## Slide 59: Performance Comparison
 | Single Cycle Design | Two Cycle Design
Critical path | 12 ns | 6.5 ns
Max clock frequency | 80 MHz | 150 MHz
Max throughput | 80 MHz | 150 MHz
Latency | 1 cycle = 12 ns | 2 cycles = 13 ns
 | Single Cycle Design | Two Cycle Design
Critical path | 12 ns | 6.5 ns
Max clock frequency |  | 
Max throughput | 80 MHz | 150 MHz
Latency | 1 cycle = 12 ns | 2 cycles = 13 ns
Pipelining benefit: For small increase in latency, we dramatically improve throughput

## Slide 60: Outline
Static Timing Analysis in Combinational Logic
Static Timing Analysis in Sequential Logic
Sequential Logic Timing Diagrams
VCD Files and Timing Diagrams from Vitis

## Slide 61: Value-Change Points
Simulation tools trace values over time for large numbers of signals
Data on each signal is typically stored via value-change points
  Value change points also called valued change events, transitions, …
Definition: A signal has value-change points if:

## Slide 62: Timing Diagram and VCDs
Timing diagrams can be drawn from the VCDs
Example with two signals:
  VC points for : {(3,5), (20,17), (40,8)}
  VC points for : {(12,3), (25,12), (35,0)}
In this plot, times are in ns

## Slide 63: Viewing Waveforms in Vivado
Vivado has a built-in waveform viewer
But no way to download the data
  Stored in a proprietary format
Can only be seen in GUI
As far as I know

## Slide 64: Viewing Timing Diagrams in this Class
Use course package xilinxutils
  Many python utilities for Xilinx tools
Demonstrate on simple function demo
  Covered in Unit 2
Sv_sim utility:
  Modifies the vitis simulation files
  Adds a VCD file
  Creates a dump.vcd file
In python:
  Load the VCD file
  Use VCD package

## Slide 65: Parsing the Signals in Python
Create a VcdParser object
Define signals to parse
Add signals to parser

## Slide 66: Displaying the Signals in Python
Create a TimingDiagram object
Add the signals from the parser
Plot

## Slide 67: Drawing Timing Diagrams in Python
Course repo contains a xilinxutils package
  Custom package in this class
  Many helper routines for Xilinx tools
Tools for parsing and visualizing VCD files
Code to produce timing diagram